## Slide 1: Intel 8085 Microprocessor Addressing Modes

## Slide 2: Addressing Modes of 8085
To perform any operation, we have to give the corresponding instructions to the microprocessor.
In each instruction, programmer has to specify 3 things:
  Operation to be performed.
  Address of source of data.
  Address of destination of result.

## Slide 3
The method by which the address of source of data or the address of destination of result is given in the instruction is called Addressing Modes.
The term addressing mode refers to the way in which the operand of the instruction is specified.

## Slide 4
Intel 8085 uses the following addressing modes:
Direct Addressing Mode
Register Addressing Mode
Register Indirect Addressing Mode
Immediate Addressing Mode
Implicit Addressing Mode

## Slide 5: 1. Direct Addressing Mode
In this mode, the address of the operand is given in the instruction itself.
LDA is the operation.
2500 H is the address of source.
Accumulator is the destination.

## Slide 6: 2. Register Addressing Mode
In this mode, the operand is in general purpose register.
MOV is the operation.
B is the source of data.
A is the destination.

## Slide 7: 3. Register Indirect Addressing Mode
In this mode, the address of operand is specified by a register pair.
MOV is the operation.
M is the memory location specified by H-L register pair.
A is the destination.

## Slide 8
MVI is the operation.
05 H is the immediate data (source).
A is the destination.
4. Immediate Addressing Mode
In this mode, the operand is specified within the instruction itself.

## Slide 9: 5. Implicit Addressing Mode
If address of source of data as well as address of destination of result is fixed, then there is no need to give any operand along with the instruction.
CMA is the operation.
A is the source.
A is the destination.

## Slide 10: Thank You Have a Nice Day